## Slide 1: Lecturer: Eng. Mahdi Obsiyeh
CCNP
Eelo University
Faculty of IT, TE, BIT
Borama, Somaliland

## Slide 2: IP-address SUBNETTING Chapter 3

## Slide 3: In this chapter, you will learn to:
  Explain the structure IP addressing and demonstrate the ability to convert between 8-bit binary and decimal numbers.
  Given an IPv4 address, classify by type and describe how it is used in the network.
  Explain how addresses are assigned to networks by ISPs and within networks by administrators.
  Determine the network portion of the host address and explain the role of the subnet mask in dividing networks.
  Use common testing utilities to verify and test network connectivity and operational status of the IP protocol stack on a host.

## Slide 4: Introduction
  An Internet Protocol address (IP address) is a numerical label assigned to each device (e.g., computer, printer) participating in a computer network that uses the Internet Protocol for communication.

## Slide 5: The Structure of an IPv4 Address
  At the Network layer, the packets need to be identified with the source and destination addresses of the two end systems.
  Each device on a network must be uniquely defined.
Dotted Decimal; Binary; Octet
  Each byte of the binary pattern, called an octet.
    Each decimal number represents one byte or 8 bits, or an octet.
  Binary address:
    10101100 00010000 00000100 00010100
  Dotted decimal address:
    172.16.4.20

## Slide 6
  There are two types of IP address
  IPv4 (32 bit)
  IPv6 (128 bit)
  IPv4 addresses consist of 32 bit
  What is a bit? Bit is either 0 or 1
  Every each 8 bit = 1 byte or 1 Octet there for IP address consist of 4 Byte and it can be represented as 8.8.8.8
  IP address can be either public IP address or private IP address
  Public IP address: is an IP address that can be accessed over the Internet. Like http://www.eelouniversity.org/
  Private IP address: Private IP address is used for internet organization, offices, campus, university, hospitals and etc.

## Slide 7
Public and Private Addresses

## Slide 8
  The IPv4 addresses are unique and universal/public.
  An IPv4 address is 32 bits long.
  The address space of IPv4 is 232 (4,294,967,296)
  Notation.
    Binary notation
    Dotted-decimal notation

## Slide 9: IP ADDRESS: is divided into two 5 classes A, B, C, D, E
CLASS | Start - End | Default subnet mask | Bit for the network | Bits for the host | Hosting
A | 1 - 126 | 255.0.0.0 | /8 bits network | 24 bits | 16.777.214 (224-2 )
B | 128 - 191 | 255.255.0.0 | /16 bits network | 16 bits | 65.534 (216-2)
C | 192 - 223 | 255.255.255.0 | /24 bits network | 8 bits | 254 (28-2)
D | 224 - 239 | Class D is used for multicasting purpose |  |  | 
E | 240 - 255 | Class E is reserved for future use |  |  | 

## Slide 11
IP address class A network, examples
IP address class B network, examples
1.2.3.0 | 20.30.10.0 | 120.120.1.0
2.3.11.0 | 30.10.20.0 | 17.19.20.0.
5.1.2.0 | 45.45.45.45. | 69.12.12.0
126.10.10.0 | 111.111.123.140. | 80.0.0.0
128.10.12.0 | 172.60.60.0 | 190.0.0.0
140.30.20.0 | 172.31.16.0 | 191.20.1.0
177.67.12.0 | 191.191.0.0 | 150.150.150.0
160.10.17.0 | 129.40.40.0 | 140.140.12.0

## Slide 12
IP address class C network, examples
192.100.100.0 | 200.0.200.0 | 223.20.100.0
193.10.20.0 | 195.195.100.0 | 222.222.222.0
199.0.13.0 | 192.168.10.0 | 198.160.160.0
210.97.92.0 | 192.168.20.0 | 209.209.10.0

## Slide 13: Private IP Address
CLASS | Start - End | Default subnet mask | Bit for the network | Bits for the host | Private IP Address starting | Private IP address End
A | 1 - 126 | 255.0.0.0 | /8 bits network | 24 bits | 10.0.0.0 | 10.255.255.255
B | 128 - 191 | 255.255.0.0 | /16 bits network | 16 bits | 172.16.0.0 172.17.0.0 172.18.0.0 172.19.0.0 upto 172.31.0.0 | 172.16.255.255 172.17.255.255 172.18.255.255 172.19.255.255 172.31.255.255
C | 192 - 223 | 255.255.255.0 | /24 bits network | 8 bits | 192.168.0.0 | 
D | 224 - 239 | Class D is used for multicasting purpose |  |  |  | 
E | 240 - 255 | Class E is reserved for future use |  |  |  | 

## Slide 14
Class A Subnet Mask | Network | Host | Host | Host
 | 255 | 0 | 0 | 0
Class A Subnet Mask | Network | Network | Host | Host
 | 255 | 255 | 0 | 0
Class A Subnet Mask | Network | Network | Network | Host
 | 255 | 255 | 255 | 0

## Slide 15: Understanding base value and position
Bit Position | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Position Value | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
In Binary | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 16
Examples of IP address in decimal notation are following: -
172.168.1.1
192.168.1.1
Examples of IP address in binary notation are following: -
10101100.10101000.00000001.00000001
11000000.10101000.00000001.00000001

## Slide 17
Examples of subnet mask in decimal notation are following: -
255.0.0.0
255.255.0.0
255.255.255.0
Examples of subnet mask in binary notation are following: -
11111111.00000000.00000000.00000000
11111111.11111111.00000000.00000000
11111111.11111111.11111111.00000000

## Slide 18: Decimal to Binary
Example 1
192. 168. 25. 0
11000000
00000000
00011001
10101000

## Slide 19
Example 2
10. 8. 255. 172
00001010
10101100
11111111
00001000

## Slide 20: Binary to Decimal
Example 3
11000000.10101000.00000001.00000001
192
1
1
168

## Slide 21
Example 4
00001100. 01100100. 10010110. 11111010
10
250
150
100

## Slide 22: What is the Subnetting
Subnetting enables the network administrator to further divide the host part of the address into two or more subnets. In this case, a part of the host address is reserved to identify the particular subnet

## Slide 23: Subnetting IPv4
Advantage of subnetting = Better IP management.
Sometimes happen that you are network administrator and managing/controlling Telesom company.
Telesom company have different sections, sales, financial, IT, management, SIM card, and cashier dept and each part have their computers and printers, If they need 70 IP address and you provide 254 IP- address, it seems that you lost many ip address (184 IP address).

## Slide 25: Stealing bits from host bits class-A
 | IP Address 192 168 10 15 |  |  |  |  |  |  |  |  |  | 
 | Subnet Mask | 255 |  |  | 0 |  | 0 |  | 0 |  | 
 |  | 1111 1111 |  |  | 0000 0000 |  | 0000 0000 |  | 0000 0000 |  | 
Weight |  |  | 128 | 64 |  | 32 |  | 16 |  | 8 | 
Borrowed Bits |  |  | 1 | 2 |  | 3 |  | 4 |  | 5 | 
Sub-Network |  |  | 2 | 4 |  | 8 |  | 16 |  | 32 | 

## Slide 26: Stealing bits from host bits class-B
 | IP Address 192 168 10 15 |  |  |  |  |  |  |  |  |  | 
 | Subnet Mask | 255 |  |  | 255 |  | 0 |  | 0 |  | 
 |  | 1111 1111 |  |  | 1111 1111 |  | 0000 0000 |  | 0000 0000 |  | 
Weight |  |  | 128 | 64 |  | 32 |  | 16 |  | 8 | 
Borrowed Bits |  |  | 1 | 2 |  | 3 |  | 4 |  | 5 | 
Sub-Network |  |  | 2 | 4 |  | 8 |  | 16 |  | 32 | 

## Slide 27: Stealing bits from host bits class-C
 | IP Address 192 168 10 15 |  |  |  |  |  |  |  |  |  | 
 | Subnet Mask | 255 |  |  | 255 |  | 255 |  | 0 |  | 
 |  | 1111 1111 |  |  | 1111 1111 |  | 1111 1111 |  | 0000 0000 |  | 
Weight |  |  | 128 | 64 |  | 32 |  | 16 |  | 8 | 
Borrowed Bits |  |  | 1 | 2 |  | 3 |  | 4 |  | 5 | 
Sub-Network |  |  | 2 | 4 |  | 8 |  | 16 |  | 32 | 

## Slide 28
Weight | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Borrowed Bits | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Sub-Network | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 255

## Slide 29
Weight | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Borrowed Bits | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Sub-Network | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 255
Prefix | /25 | /26 | /27 | /28 | /29 | /30 | /31 | /32
Hosts (2^n – 2 =) | 126 | 62 | 30 | 14 | 6 | 2 | 0 | 0
PREFIX TO SUBNET MASK

## Slide 33
Block Size | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Borrowed Bits | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Sub-Network | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 255
Prefix | /25 | /26 | /27 | /28 | /29 | /30 | /31 | /32
Hosts | 126 | 62 | 30 | 14 | 6 | 2 | 0 | 0
Subnet mask | 128 | 192 | 224 | 240 | 248 | 252 | 254 | 255

## Slide 34: Prefix to Block
8
16
24
32
1 | 9 | 17 | 25 | = | 128
2 | 10 | 18 | 26 | = | 64
3 | 11 | 19 | 27 | = | 32
4 | 12 | 20 | 28 | = | 16
5 | 13 | 21 | 29 | = | 8
6 | 14 | 22 | 30 | = | 4
7 | 15 | 23 | 31 | = | 2
8 | 16 | 24 | 32 | = | 1
25
26
27
28
29
30
31

## Slide 35
Classless Inter-Domain Routing
(CIDR)
/1 | 128.0.0.0 |  | /9 | 255.128.0.0 |  | /17 |  | 255.255.128.0 |  |  | /25 | 255.255.255.128 | 
/2 | 192.0.0.0 |  | /10 | 255.192.0.0 |  | /18 |  | 255.255.192.0 |  |  | /26 | 255.255.255.192 | 
/3 | 224.0.0.0 |  | /11 | 255.224.0.0 |  | /19 |  | 255.255.224.0 |  |  | /27 | 255.255.255.224 | 
/4 | 240.0.0.0 |  | /12 | 255.240.0.0 |  | /20 |  | 255.255.240.0 |  |  | /28 | 255.255.255.240 | 
/5 | 248.0.0.0 |  | /13 | 255.248.0.0 |  | /21 |  | 255.255.248.0 |  |  | /29 | 255.255.255.248 | 
/6 | 252.0.0.0 |  | /14 | 255.252.0.0 |  | /22 |  | 255.255.252.0 |  |  | /30 | 255.255.255.252 | 
/7 | 254.0.0.0 |  | /15 | 255.254.0.0 |  | /23 |  | 255.255.254.0 |  |  | /31 | 255.255.255.254 | 
/8 | 255.0.0.0 |  | /16 | 255.255.0.0 |  | /24 |  | 255.255.255.0 |  |  | /32 | 2255.255.255.255 | 
128 |  | 64 |  | 32 | 16 |  | 8 |  | 4 | 2 |  | 1 | 0

## Slide 36: Variable-Length Subnet Masking (VLSM)
Variable-Length Subnet Masking (VLSM) amounts to “Subnetting subnets," which means that VLSM allows network engineers to divide an IP address space into a hierarchy of subnets of different sizes, making it possible to create subnets with very different host counts without wasting large numbers of addresses

## Slide 37
Network | Host | Block Size | Network Address | Subnet Mask
1 | 2 | 4 | 192.168.10.0/30 | 255.255.255.252
2 | 2 | 4 | 192.168.10.4/30 | 255.255.255.252
3 | 2 | 4 | 192.168.10.8/30 | 255.255.255.252
4 | 2 | 4 | 192.168.10.12/30 | 255.255.255.252
5 | 30 | 32 | 192.168.10.32/27 | 255.255.255.224
6 | 8 | 16 | 192.168.10.16/28 | 255.255.255.240
7 | 12 | 16 | 192.168.10.224/28 | 255.255.255.240
8 | 30 | 32 | 192.168.10.192/27 | 255.255.255.224
9 | 60 | 64 | 192.168.10.64/26 | 255.255.255.192
10 | 45 | 64 | 192.168.10.128/26 | 255.255.255.192
Variable Length Subnet Mask
(VLSM)

## Slide 38
128.64.32.16.8.4.2.1 - 128.64.32.16.8.4.2.1 - 128.64.32.16.8.4.2.1 - 128.64.32.16.8.4.2.1
/24 | 255 | 255 | 255 | 0
/25 | 255 | 255 | 255 | 128
/26 | 255 | 255 | 255 | 192
/27 | 255 | 255 | 255 | 224
/28 | 225 | 255 | 255 | 240
/29 | 225 | 255 | 255 | 248
/30 | 255 | 255 | 255 | 252

## Slide 39: Network formula
Network | 2N
host | 2N -2
Network address | 
Frist host | 
Last host | 
Broad cast address | 

## Slide 40: /25
Network = | 21 | 2 network | 
Host = | 27 - 2 | 128 -2 = 126 host | 
Network address = | 256-128 | 0 | 128
Frist host = |  | 1 | 129
Last host = |  | 126 | 254
Broadcast address = |  | 127 | 255

## Slide 42: /26
Network = | 22 | 4 network |  |  | 
Host = | 26 - 2 | 64 -2 = 62 host |  |  | 
Network address = | 256-192 | 0 | 64 | 128 | 192
Frist host = |  | 1 | 65 | 129 | 193
Last host = |  | 62 | 126 | 190 | 255
Broadcast address= |  | 63 | 127 | 191 | 256

## Slide 44: Class-ACTIVITY
/27 and /28
Network = |  |  |  |  | 
Host = |  |  |  |  | 
Network address = |  |  |  |  | 
Frist host = |  |  |  |  | 
Last host = |  |  |  |  | 
Broadcast address = |  |  |  |  | 

## Slide 45: Subnetting

## Slide 46: Home work Assignment
DO THIS class A subenetting mask
/4
/9
/13
Do this class B subnetting mask
/18
/20
/23
Do this class C subnetting mask
/28
/29
/30

## Slide 47
End